## Slide 1
Automation of Very Large Scale Network Deployment
Matthew Taylor
Network Automation Consultant
matttaylor5060@gmail.com

## Slide 2
Here’s the problem
matttaylor5060@gmail.com
How can we do this?
You have over 10,000 remote sites
You want to migrate them all to a new WAN and install a new remote site router and LAN switches
You MUST achieve this in 9 months.

## Slide 3
No pre-installation of site specific configurations to the remote site equipment (allowing any equipment to be shipped to any site)
The Plan
matttaylor5060@gmail.com
Avoid the need for the on-site installation engineer to load site-specific configurations or connect to the remote site equipment (to access larger pool of non-cisco aware installation engineers)
In other words have identical configurations on all equipment
Automate the loading of site specific configurations and testing during the engineering visit.

## Slide 4
Commissioning Helpdesk Console
10 – Hi. I am in the remote site 111111, and the serial number of the new Cisco router is GR1234567.
PPP based Access
e.g. DSL
Existing Router
Management
Network
LINUX Script Server
Console Session
from Helpdesk staff laptop to script server
Remote Site
Staging Centre
PPP tunnel
Key
1 Receive site-specific data from customer
int fa0/0
ip address
2 Generate site specific router config for each remote site
3 Load site specific configs with site ID into Script Server
4 Stage remote site routers with identical base config.
NNI
…and install new
Cisco router
6 PPP tunnels builds to NNI
7 Router authenticates to NNI using username and password from its initial configuration (Radius), and gets a unique IP address allocated from a pool by the NNI for use on the PPP link.
8 script continually pings initial PPP IP address pool.
9 If a new router on initial config is discoverred retrieve its serial number via SNMP and present to Helpdesk console.
Site A 111111
12 Push site specific config to router`s startup config and reload.
Migration Day
Prior to Migration
5 Remove Existing router
Commissioning Helpdesk
10.1.1.12 GR1234567
16 Config located (or generated)
Site Live
Backup
e.g.
3G/4G
3G/4G radio link
Apps
Data Centres
WAN
13 Automated testing of primary and backup paths. Results provided to Helpdesk.
11 Commissioning Desk enter Site ID for Serial number into console
Site ID Postal Address Site Specific IP Addressing
111111 Site A 10.10.10.0 / 26
222222 Site B 10.20.20.0 / 26
333333 Site C 10.30.30.0 / 26
Site ID config
111111
222222
333333
GR1234567
matttaylor5060@gmail.com

## Slide 5
Triggered by commissioning Helpdesk staff:
matttaylor5060@gmail.com
Linux Scripts
Scheduled:
Site Pre-Checks -
Linux bash script using an Expect program to login to remote site equipment and perform checks (IOS, build, new config not live). Could use Python and Pexpect.
Config - Generation
Python script to merge site specifics with configuration templates
Linux bash script to ping IP pool and then SNMP poll for serial number if get a reply.
Site Discovery -
Copy new config - to remote
Linux bash script using an Expect program to scp copy new config to remote site startup-config and reload.
Site Post-Checks -
Linux bash script using an Expect program to login to remote site and do tests (ping, interface stats, backup tests). Credentials.

## Slide 6
matttaylor5060@gmail.com
Key script code
SNMP get serial number (Bash):
serial_number=`snmpwalk -v2c -c $snmp_cummunity_string $ip_address .iso.3.6.1.4.1.9.3.6.3 | cut -f 2 -d "\""`
Login to router (Expect):
#!/usr/bin/expect
set ip [lindex $argv 1]
set login_id [lindex $argv 2]
set first_password [lindex $argv 3]
set ssh_pid [spawn -noecho ssh -l $login_id $ip]
expect {
“passsword:” {
send “$first_password\r”
…
“yes” {
send “yes\r”
…
default {
puts "FAILED - to connect to $ip with ssh. Killing ssh pid\n"
exec kill $ssh_pid
}
}

## Slide 7
#!/usr/bin/expect
set filename [lindex $argv 4]
set filePointer [open $filename r]
set fileData [read $filePointer ]
set commandLines [split $fileData "\n"]
set results ""
set prompt "(>$)|(#$)|(> $)|(])"
foreach line $commandLines {
send "$line\r"
expect -re "$prompt"
append results $expect_out(buffer)
}
set resultsFile [open "results.$ip.out" w]
puts $resultsFile $results
matttaylor5060@gmail.com
Execute commands from a file on remote device (Expect):
Key script code

## Slide 8
matttaylor5060@gmail.com
scp copy a config to a remote device’s startup (Expect):
#!/usr/bin/expect
set ip [lindex $argv 0]
set source_file_name [lindex $argv 1]
set destination_file_name [lindex $argv 2]
set resultsFile [open "results.$ip.out" w]
set results ""
spawn scp $source_file_name $scp_username@$ip:"startup-config"
expect {
”password:" {
send "$scp_password\r"
expect "closed"
}
"yes" {
send "yes\r"
expect ”password:"
send "$scp_password\r"
expect "closed"
}
}
append results $expect_out(buffer)
puts $ resultsFile $results
close $ resultsFile
Key script code

## Slide 9
matttaylor5060@gmail.com
Ansible approach
Could this be done in Ansible / Ansible Tower so that change control and governance is standardised.
Some challenges of using native Ansible: need for complex Logic and string manipulation.
Perhaps use Ansible to run the other scripts.

## Slide 10
matttaylor5060@gmail.com
interface ATM<>
description - ADSL
no ip address
pvc <>/<>
encapsulation aal5mux ppp dialer
dialer pool-member 1
!
!
interface Dialer<>
ip address negotiated
encapsulation ppp
dialer pool 1
ppp chap hostname <>
ppp chap password <>
!
Key configs for dynamic IP addressing (cisco, DSL example)
Remote site router (identical)

## Slide 11
aaa authentication ppp <> group <>
aaa authorization network <> group <>
!
vpdn enable
vpdn search-order domain
vpdn-group <>
accept-dialin
virtual-template 1
!
interface Virtual-Template1
no ip address
peer default ip address pool init_ip_pool
ppp authentication chap pap <>
ppp authorization <>
!
ip local pool init_ip_pool <from> <to>
NNI router
Key configs for dynamic IP addressing (cisco, DSL example)
matttaylor5060@gmail.com

## Slide 12
Github: https://github.com/matttaylor5060/largeScaleAutomation
Email: matttaylor5060@gmail.com